## Slide 1: The Spectre of a Meltdown
Mohan Parthasarathy
Technical Architect, HPE
October 11th, 2019

## Slide 2: Prelude – A déjà vu Moment
If ( The audience does not know about spectre or meltdown)
Talk about Spectre and Meltdown
else
Let us all just go home 

## Slide 3: Agenda
Background for the attacks
Spectre and Meltdown explained
More attacks..
Linux after the attacks

## Slide 4: The origins of the Meltdown
Moore’s Law - Every ~2 years: 2x transistors, 1.4x faster. How do you keep up ? Do more per clock
  Reduce impact of memory delays through caching
  Keep CPU busy during delays using Speculation
The need for caching
  Typical x86 systems have a socket connected to an IMC with multiple DDR4 channels. A Xeon v4 E5 socket has a maximum memory b/w of 76.8 GB/s (4 memory channels at DDR4-2400).
  A 3.5 GHz pipeline that retires around 4 x86 instructions per cycle (around 16 bytes) has to be fed at around 56GB/s/core
The need for speculation
  The L1/L2/L3 latencies for modern Xeon processors are in the 4/12/44 cycles range
  Branches can stall the pipeline

## Slide 5: The Invisible (or is it ?) Micro-architecture
Caches are not directly visible to applications.
Instructions executed out-of-order but retired in-order
Speculation not committed unless correct. Transient execution discarded.
Exploitation : Spectre type attacks and Meltdown type attacks
Spectre | Meltdown
Control and Data misprediction exploits | Deferred Permission Checks on Faulting Instructions
Transient instructions only compute on accessible data | Transient instructions compute across privilege levels
More of a design side effect | More of an implementation failure
Requires gadgets in victim code like kernel | Attacks possible from user space

## Slide 6: Core Micro-architecture
L1 $
Instruction Decode
Branch Prediction
L2 $
Micro op cache
Out of order engine
Load Buffers
LFBs
Store Buffers
ROB
Retirement Unit
CORE
Memory
Exe
Load
Store
ALU
ALU
Execution Unit

## Slide 7: Spectre v1 (Conditional Branch)
The Spectre attacks are about exploiting speculative execution in processors
Speculative Execution is about guessing likely future execution paths and prematurely executing instructions in them.
Spectre attacks depend on architectural state such as caches not being reverted back on incorrect speculation.
Impacts most modern processors, including Intel x86, ARM, AMD, IBM Power etc.
Typically exploits existing code in the kernel (syscalls for instance)
Attack Methodology :
  Code Snippet (Gadget in Kernel Code) :
    If (x < array1_size)
    y = array2[array1[x] * 256]
where x contains attacker controlled data
  Flush the array1_size and all of array2
  Pass large x to code to offset to desired location in memory where secret lies
  Reload iteratively from array2 to check existence in cache. The index of array2 that is cached is the secret.
Notes: E.g : When a conditional branch depends on an uncached value located in memory, it may take several 100 clock cycles before the value becomes known. Instead of idling, the processor can guess the direction of control flow. If the guess was wrong, the processors discard the speculative execution by reverting to the state saved when the speculation started.

## Slide 8: Spectre v2 (Branch Target Injection)
Exploits the fact that branch prediction can be primed and faked.
Attack Methodology :
  Code Snippet (Gadget in Kernel Code) :
    if (untrusted_offset_from_user< array1->length) {
    user_injected_target:
    unsigned char value = array1->data[x] ;
    unsigned long index2 = ((value&1)*0x100)+0x200;
    if (index2 < array2->length) { unsigned char value2 = array2->data[index2] ; } }
  Flush the array1->length and all of array2
  Poison branch target.
  Pass large x to code to offset to desired location in memory where secret lies
  Reload iteratively from array2 to check existence in cache. The index of array2 that is cached is the secret.
Notes: E.g : When a conditional branch depends on an uncached value located in memory, it may take several 100 clock cycles before the value becomes known. Instead of idling, the processor can guess the direction of control flow. If the guess was wrong, the processors discard the speculative execution by reverting to the state saved when the speculation started.

## Slide 9: Spectre v4 (Speculative Store Bypass)
Exploits the fact that loads can pass stores transiently.
Attack Methodology :
  Code Snippet (Gadget in Kernel Code) :
    X = &Key; // Attacker manages to get variable with address of Key stored into pointer X
    <at some later point>
    X = &M; // Does a store of address of M to pointer X
    Y = array[*X & 0xFFFF]; // Dereferences address of M which is in pointer X but gets key K
  Reload iteratively from array to check existence in cache. The index of array1 that is cached is the secret.
Notes: E.g : When a conditional branch depends on an uncached value located in memory, it may take several 100 clock cycles before the value becomes known. Instead of idling, the processor can guess the direction of control flow. If the guess was wrong, the processors discard the speculative execution by reverting to the state saved when the speculation started.

## Slide 10: Meltdown (v3)
The Meltdown attack is a similar attack which exploits out-of-order execution on processors. Speculation is a more restricted form of out-of-order execution related to conditional branches and branch predictions.
It relies on the observation that when an instruction causes a trap, following executions that were executed out-of-order are aborted.
It also exploits a vulnerability specific to Intel x86 processors due to which speculatively executed instructions can bypass memory protection.
This allows access to kernel memory from user space. The access causes a trap but before the trap is issued, code that follows the access leaks information through the cache similar to spectre.
Impacts mainly Intel x86 but Power also seems to be vulnerable to a smaller extent.
Code Snippet :
rcx=kernel address; rbx=probe_array;
retry :
mov al, byte[rcx]
shl rax, 0xc;
jz retry
mov rbx, qword [rbx + rax]
Notes: E.g : When a conditional branch depends on an uncached value located in memory, it may take several 100 clock cycles before the value becomes known. Instead of idling, the processor can guess the direction of control flow. If the guess was wrong, the processors discard the speculative execution by reverting to the state saved when the speculation started.

## Slide 11: Meltdown continued..
Foreshadow/Meltdown-P (PTE bit manipulation to access physical memory)
Foreshadow-NG/L1TF
  Exploits the speculative execution during a page fault when the present bit is cleared for a PTE
  Fix : L1D cache flush on privilege boundaries
LazyFP
Meltdown-GP (Variant 3a/System Register Bypass) – rdmsr
RIDL (Line Fill Buffer)/ZombieLoad (Line Fill Buffer)
  Exploits in-flight data in the Line Fill Buffers (LFBs)
Fallout (Store Buffers)
  Exploits in-flight data in the Store Buffers (SBs)

## Slide 12: Summary of Exploits
Vulnerability | A.K.A | Type | Mitigation
Spectre v1 (CVE-2017-5753) | Bounds check bypass | Spectre | Addressed through speculation barriers at user/kernel boundaries (lfence/new ucode ops) Ibrs_enabled
Spectre v2 (CVE-2017-5715) | Branch Target Injection | Spectre | Hardware(IBPB, IBRS, STIBP), Software(retpoline)
Meltdown (CVE-2017-5754) | Rogue Cache Handling | Meltdown | Addressed through page table isolation (PTI). KAISER patch.
Spectre v3a (CVE 2018-3640) | Rogue System Register Read | Spectre | Processor Microcode Update
Spectre v4 (CVE 2018-3639) | Speculative Store Bypass | Spectre | microcode-based mitigation referred to as Speculative Store Bypass Disable (SSBD)
L1TF, Foreshadow (CVE 2018-3615, 3620, 3646) | L1 Terminal Fault | Meltdown | L1D cache flush on privilege boundaries
RIDL (CVE 2018-12130) | MFBDS | Meltdown | L1D cache flush on privilege boundaries
Fallout (CVE 2018-12126) | MSBDS | Meltdown | L1D cache flush on privilege boundaries
Zombie Load (CVE 2018-11091) | MDSUM/MLPDS | Meldown | L1D cache flush on privilege boundaries

## Slide 13: Linux after the holocaust
Boot Options : spectre_v2=off spec_store_bypass_disable=off pti=off l1tf=off nospectre_v1 mds=off
$ grep . /sys/devices/system/cpu/vulnerabilities/* /sys/devices/system/cpu/vulnerabilities/meltdown:Mitigation: PTI /sys/devices/system/cpu/vulnerabilities/spectre_v1:Vulnerable /sys/devices/system/cpu/vulnerabilities/spectre_v2:Vulnerable: Minimal generic ASM retpoline
Co-scheduling SMT threads work
Performance Impacts
  Spectre/Meltdown initial estimates: 8-19% performance impact depending on workload
  Retpoline support revised this to 4-8% (based on updated/recompiled kernels)
  Some of the microcode mitigations like IBRS have shown more than 20% impact on benchmarks like sysbench
  L1TF mitigations (cache flushes across contexts) have shown around 3-31% impact on SPEC.

## Slide 14: Thank you
Contact information