## Slide 1
Micro-architectural Attacks:
Where Security meets
Computer Architecture
Debdeep Mukhopadhyay
Professor
Secured Embedded Architecture Laboratory (SEAL)
Department of Computer Science and Engineering
IIT Kharagpur
debdeep@cse.iitkgp.ac.in
debdeep.mukhopadhyay@gmail.com

## Slide 2: JOINT WORK WITH
Prof Chester Rebeiro
Dr Sarani Bhattacharya

## Slide 3
Side Channel Infrastructure at IIT Kharagpur
Power Analysis
Fault Analysis
EM Analysis
Laser Injections
Cache Analysis
http://cse.iitkgp.ac.in/resgrp/seal/

## Slide 4: (In)Security Analysis of IoT at IIT Kharagpur
  Description
    IoT Lab introduces relatively new research platform at IIT Kharagpur which is focused towards research, learning and hands-on experimentation on the promising Internet of Things.
  On going Experiments
      Design of PUF based secure mutual authentication and communication protocol for IOT applications.
      Exploiting the security vulnerabilities in
      Philips Hue Lighting system.
      Exploiting the security vulnerabilities of
      a video surveillance system using Wifi.
  Equipments Available
      Philips Hue light system
      Intel Edison board
      Nexys 4 DDR
      Logitech HD Camera
      Rasberry Pi Kit
      HP Wireless network printer

## Slide 5: Incubation on Embedded Security
Embedded Security and Privacy Pvt Ltd.
Contacts:
  Dr Debdeep Mukhopadhyay, debdeep@cse.iitkgp.ernet.in
  Dr Shivam Bhasin, NTU Singapore, sbhasin@ntu.edu.sg
Visit: http://esp-research.com/
Crypto-Libraries
Security Evaluation
Consulting and Training
Cloud Security
IoT Security

## Slide 6: Imaging based Trojan Detection and Reverse Engineering
Recently procured FIBS/SEM installed in IIT KGP

## Slide 7: Research Focus of SEAL, IIT Kharagpur
5
http://cse.iitkgp.ac.in/resgrp/seal/
Secured Embedded
Architecture Laboratory (SEAL)
Side Channel
Analysis
VLSI
Of
Cryptosystems
Physically
Uncloneable
Functions
Trojan Design
&
Detection
Countermeasure
Designs
Formal
Verification
For
Finite Field
Circuits
Micro-architectural
Attacks
Crypto-systems
for
Cloud
&
IoT
Machine Learning
for Attacks
& Defences

## Slide 8: Outline
Part I: Bird’s Eye View
Part II: Cache Timing Attacks on Block Ciphers
Part III: Quest for Ideal Implementations against Cache Timing Attacks
Part IV: Modern Times

## Slide 9: Part I
Background and Bird’s eyeview

## Slide 10: Software and Hardware
Computer hardware are the physical parts or components of a computer, such as the central processing unit, monitor, keyboard, computer data storage, graphic card, sound card and motherboard.
Software comprises of instructions that can be stored and ran by hardware.
Are they related?
Or are they two different
Disciplines?

## Slide 11: Two sides of the “computation coin”
This seemingly disparate sub-disciplines of computer science, software and hardware, are intrinsically related.
Though in many schools there is an explicit marked separation and the single subject is organized for pedagogy and research as:
  Computer Science
  Computer Engineering

## Slide 12: Micro-architectural Attacks: Security cannot be an afterthought
Sarani Bhattacharya and Debdeep Mukhopadhyay, “Who watches the watchmen?:
Utilizing Performance Monitors for Compromising keys of RSA on Intel Platforms”, CHES 2015.
Strong correlation between two-bit predictor
and system branch predictor
Partitioning Ciphertexts set based on
simulated Branch miss Modelling
Branch misprediction values from Hardware Performance Counter revealing the secret exponent bit of RSA
To quote Bruce Schneier, "These are side-channel attacks where one process can spy on other processes. They affect computers where an untrusted browser window can execute code, phones that have multiple apps running at the same time, and cloud computing networks that run lots of different processes at once. Fixing them either requires a patch that results in a major performance hit, or is impossible and requires a re-architecture of conditional execution in future CPU chips. It shouldn't be surprising given that microprocessor designers have been building insecure hardware for 20 years. What's surprising is that it took 20 years to discover it."
Spectre and Meltdown, Daniel Gruss, Moritz Lipp, Yuval Yarom, Paul Kocher, Daniel Genkin, Michael Schwarz, Mike Hamburg, Stefan Mangard, Thomas Prescher and Werner Haas, Google Ground Zero Project.

## Slide 13: Security can be a game changer!

## Slide 14: Part-II
Looking into Micro-architecture Attacks
: Timing Attacks on Block Ciphers
Chester Rebeiro, Debdeep Mukhopadhyay, Junko Takahashi, Toshinori Fukunaga:Cache Timing Attacks on Clefia. INDOCRYPT 2009: 104-118

## Slide 15: What are Side Channels?
These are covert channels which leak information which the designers of cryptographic algorithms did not consider.
Information is leaked because of the implementation:
  optimization leads to information leakage
  example: an if-else statement in a programming language

## Slide 16: Micro-architectural Leakage Models
Side channel leakage due to the underlying computer architecture.
However leakage (in general) can be a function of several parameters:
  Branch prediction algorithms
  Hyperthreading
  Memory Technology
  Cache Architecture
These are more relevant for software based attacks.
Cache
Attacks
Our Focus

## Slide 17: Square and Multiply Algorithm
We assume that the attacker knows the first b-1 bits, and wants to obtain the b-1th bit of the secret key.
Attacker knows x[0],…,x[b-2] and wants to determined x[b-1]
Paul C Kocher, Timing Attacks on Implementations of Diffie-Hellman, RSA, DSS and Other Systems, In Proceedings of Crypto, LNCS 1109, pgs 104-113, 1996.

## Slide 18: Timing Measurement
Assume that the attacker can measure time accurately for a function P.
Compute the timestamp before and after calling a function P
Then evaluate the difference between the timestamps.
Note if there is no program between two timestamp calls, there is still a small time difference.
This overhead should be appropriately deducted after computing the running time of the program P.

## Slide 19: Timestamp Snippet

## Slide 20: Attack Methodology
Attacker measures the time required to perform the loop a large number of times by varying the value of y.
Each observed timing can be denoted as where is the time required for performing multiplication and squaring for bit i.
The measurement error, loop overhead are other sources of inaccuracies.
We assume that the attacker knows or has correctly evaluated in the previous iterations the first (b-1) bits: x[0],…,x[b-2]
Now the attacker guesses x[b-1]. Is it correct? 0 or 1?

## Slide 21: Attack Methodology (contd.)
If the guess is correct, subtracting from T yields
Attacker obtains a distribution by varying the value of y and observing the above timing .
Assuming that the measurement error and the individual timings for the modular multiplier are independent, the variance of this distribution is:
  If the guess is correct:
  If the guess is wrong:
The correct key bit is decided by observing the variance of the distribution of the time difference.
Idea used: Correct Guess => Decrease in variance

## Slide 22: Timing Channels in Cryptography due to Cache Memories
Bob
(Cipher)
Alice
(Adversary)
Monitor Time
Secret
Key
Microprocessor
Main Memory
Cache Memory
If there is a Cache Hit
  Access time is less
If there is a Cache Miss
  Access time is high
Why is “time” a channel for Information Leakage?
Adversary wants to get Bob’s secret key

## Slide 23: Time-Driven Cache Attack Principle
  If cache hit (less time) :
Table
Table
  If cache miss (more time):
(Adversary)
Part of a Cipher
P0
,P4
Notes: Sbox is generally implemented as a table
23

## Slide 24: Classes of Cache Attacks
Three ways to identify cache behavior
Cache Trace Attacks
Cache Access Attacks
Cache Timing Attacks

## Slide 25: Cache Trace Attacks
The Power Profile of the system gives away cache behavior.
Without Cache Miss
With Cache Miss

## Slide 26: Cache Access Attacks : Osvik’s Attack
Uses a spy program to determine cache behavior
Microprocessor
Spy
AES
Memory
Cache Memory
Part of the cache memory occupied by tables
Cache Miss
Cache Hit

## Slide 27: Cache Timing Attack
Based on measuring the total time for encryption.
Used to attack a remote server.
Server running Encryption Software
Remote Attacker
Network
Trigger Encryption &
Measure time taken

## Slide 28: Bernstein’s Cache Timing Experiment
AES
Random
P0 = 00 - FF
Cipher Text
Characteristic of Plaintext Byte P0
(Deviation from mean time)

## Slide 29: Bernstein’s Cache Timing Attack
Put key to all ZEROs and perform experiment
29
Repeat experiment with unknown key
Correlate the two results

## Slide 30: Why Cache Attacks Work on AES
The AES Structure
  Add initial Key
  Nine Rounds of
    Byte Substitution
    Shift Row
    Mix Column
    Add Round Key
  Final Round
    Byte Substitution
    Shift Row
    Add Round Key
Substitute 16 bytes from a 256 byte lookup table
Chester Rebeiro, Mainack Mandal, Debdeep Mukhopadhyay, "Pinpointing Cache Timing Attacks on AES", VLSID 2010,

## Slide 31: Software Implementations of AES (OpenSSL)
Merges all round operations into 4 lookups.
Uses 4 tables T0, T1, T2, T3 , each of size 1024 byte.
The Software Structure is
Round1:
Round2:

## Slide 32: AES Execution Time for 4KB Table
Cache Attack works because of varying execution time.
Since, Nt = Nm + Nh

## Slide 33: AES Execution Time with 256Byte Table
  …… Encryption Time is a constant
Cache Attacks
believed to be difficult

## Slide 34: Osvik’s Attack on AES-with 256B Table
Won’t Work!!!
Microprocessor
Spy
AES
Memory
Cache Memory

## Slide 35: Bernstein’s Attack on Small Tables
Large
Tables
Small
Tables
Lesser deviations in Encryption Time

## Slide 36: Some Opinions on Cache Timing Attacks
[Kelsey. et.al., 2000, Section 7]
“We believe attacks based on cache hit ratio in large Sbox ciphers like Blowfish, CAST and Khufu are possible”
We now show that cache attacks are possible even on ciphers with small sboxes
Chester Rebeiro, Debdeep Mukhopadhyay, Junko Takahashi and Toshinori Fukunaga, "Cache Timing Attacks on Clefia", Indocrypt 2009.

## Slide 37: Analysis of Cache Timing Attacks
Processor’s aim : Reduce the miss penalty
Techniques used to achieve this are
  Speculative Loading
  Prefetching
  Out-of-order loading
  Parallelization
  Overlapping

## Slide 38: Speculative Loading
Speculative Loading :Loading of data into processor before preceding branches are resolved.
  Effect on Cipher Execution :None, since branches are generally not used in block ciphers.

## Slide 39: Out-of-Order Loading
Data accessed in an order not strictly specified by the program.
LOAD AX, #1000
LOAD BX, #2000
LOAD CX, #3000
LOAD DX, #4000
LOAD DX, #4000
LOAD BX, #2000
LOAD AX, #1000
LOAD CX, #3000
Program
Execution

## Slide 40: Out-of-Order Loading on a Cipher
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
Round 1
Round 2
Out of order loading works only within a round & not between rounds.

## Slide 41: Parallelization & Overlapping
Parallelization : Two or more cache misses are serviced simultaneously.
Overlapping : Memory reads are pipelined.
Effect on Cipher Execution :
Consider a 5 round block cipher with 4 misses
Time(E1) < Time(E2)
2 misses
1 miss
1 miss
0 misses
0 misses
1 miss
1 miss
1 miss
0 misses
1 miss
E1
E2

## Slide 42: Extending Cache Timing Attack to Work on Small Table Ciphers
Challenges:
1. The deviation in encryption time is too less.
2. Timing measurements need to be more accurate.

## Slide 43: Improvements to the Timing Attack (1)
Improving Timing Measurements
  Use ‘RDTSC’ instruction to measure timing.
    This is prone to errors due to processor pipeline and out-of-order execution.
  Also use ‘CPUID’ before calling RDTSC
    This flushes the processor pipeline.
    Hence all RDTSC instructions done on a fresh pipeline.

## Slide 44
Vary only those bytes which go to the same sbox as P0.
S1
XOR
P0
K0
S2
XOR
P1
K1
S1
XOR
P2
S2
XOR
P3
K3
K2
AES
Random
P0 = 00 - FF
Constant
Improvements to the Timing Attack (2)

## Slide 45: Attack on CLEFIA
CLEFIA is a block cipher designed by Sony Corporation
It has small tables of 256 bytes.
There are 18 rounds in the cipher
  each round has 8 look-ups
  there are 2 S Boxes of 256 bytes
  Thus there are 4 look-ups per S-box in each round.

## Slide 46: CLEFIA Attack Results
On Intel Core 2 Duo, the first phase of the attack takes 1300 seconds,
Second phase (with secret key) takes 312.5 seconds
The attack has also been tested successfully on
Pentium 4
Intel Atom
Xeon – Core 2 Server
The attack fails on Pentium 3
Chester Rebeiro, Debdeep Mukhopadhyay, Junko Takahashi and Toshinori Fukunaga, "Cache Timing Attacks on Clefia", Indocrypt 2009.

## Slide 47: Correlation Results on CLEFIA
47

## Slide 48: Part-III
Looking into Micro-architecture Attacks
: An Ideal Implementation for Cache Timing Attacks
Chester Rebeiro, Debdeep Mukhopadhyay:Micro-Architectural Analysis of Time-Driven Cache Attacks: Quest for the Ideal Implementation. IEEE Trans. Computers 64(3): 778-790 (2015)

## Slide 49: Ideal Implementation against Time-Driven Cache Attacks
T
P0
K0
T
P4
K4
Block Cipher
Random
P0
Cipher Text
P4
  Suppose
  (K0 = 00 and K4 = 50)
P0 = 0, all other inputs are random
Make N time measurements
Segregate into Y buckets based on value of P4
Find average time of each bucket
Find deviation of each average from overall average (DOM)
P4 | Average Time | DOM
00 | 2945.3 | 1.8
10 | 2944.4 | 0.9
20 | 2943.7 | 0.2
30 | 2943.7 | 0.2
40 | 2944.8 | 1.3
50 | 2937.4 | -6.3
60 | 2943.3 | -0.2
70 | 2945.8 | 2.3
: | : | :
F0 | 2941.8 | -1.7
Average : 2943.57
Maximum : -6.3

## Slide 50: Different DOM for Different Implementations
Implementation | Difference of Means
AES (OpenSSL 0.9.8a ) | -6.5
DES (PolarSSL 1.1.1 ) | +11
CAMELLIA (PolarSSL 1.1.1) | 19.2
CLEFIA (Ref. Implementation 1.0) | 23.4
Easiness to attack

## Slide 51: Effect of Micro-architecture in Cache Memory in Superscalar Processors
Assume the cache is clean before executing a snippet
Snippet A
Snippet B
Snippet A !!!
Which is faster?
In Superscalar processors cache misses can be
pipelined and parallelized provided there are no memory
dependencies

## Slide 52: Which Implementation is Faster in a Superscalar Processor?
Snippet B
Snippet A
Cache misses in Snippet A can be
pipelined and parallelized
time
time

## Slide 53: Memory Access in a Cipher
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
Round 1
Round 2
Round 1
Round 2
In a cipher, memory accesses within a round can
be parallelized and pipelined. But memory accesses
across rounds should be serialized
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T

## Slide 54: A Model for Block Cipher Implementations
Table Accesses

## Slide 55: Finding the Ideal Implementation
Estimating the difference of means
Estimate the execution time with a collision
Estimate the execution time without the collision
Find the difference

## Slide 56: Time for a Round of Execution
is the latency for the first miss
the number of cache misses in the round
the latency for the subsequent misses

## Slide 57: Ideal Implementation
Ideal
Table size influences
the DOM
(such as in AES)
Micro-architectural features have a high influence on DOM
(such as in CLEFIA)
Chester Rebeiro, Debdeep Mukhopadhyay:Micro-Architectural Analysis of Time-Driven Cache Attacks: Quest for the Ideal Implementation. IEEE Trans. Computers 64(3): 778-790 (2015)

## Slide 58: A Model for Block Cipher Implementations
Table Accesses

## Slide 59: Average Cache Misses per Round (mr)
Mathematical Model
Access/Round
Size of Tables
Round Number
Cache Line Size
Average
Cache Misses for the round

## Slide 60: Average Time for Encryption
Average time for Round 1
Average time for Round 2
Average time for Round 3
Average time for Round 4
Average time for Last Round
Total time for Encryption

## Slide 61: Comparing Cipher Implementations
Test Platform :
  8 core Intel Xeon 2.13GHz
  Depends on the executing core
Cipher Implementations
  AES - OpenSSL (0.9.8ka)
  DES - PolarSSL (1.1.1)
  CAMELLIA - PolarSSL (1.1.1)
  CLEFIA – Reference Code of Sony (1.0)

## Slide 62: Different Avatars for Clefia

## Slide 63: Practical Validations
Success of the Attack vs Number of Measurements Made
Implementations identified by
the mathematical model
are more difficult to attack

## Slide 64: More Experiments
With CLEFIA and CAMELLIA on different platforms
Test platform E5606: Intel 8 core Xeon 2.13GHz, running Ubuntu 12.04
Test platform E5345 : Intel 4 core Xeon 2GHz, running Fedora OS

## Slide 65: Two Sources of Leakage
In superscalar processors there are two sources of leakage
  Leakage due to cache misses has a negative effect
  Leakage due to micro-architectural features has a positive effect
Ciphers can be designed so that the two leakages cancel each other
This allows building implementations more protected against time-driven cache attacks

## Slide 66: Patent

## Slide 67: Part-IV
Modern Times:
Timing Attacks in Modern Systems

## Slide 68: Timing Attack in Modern Systems
In modern day systems timing attack faces difficulties because of the modifications for performance improvements.
Timing measurements for the execution of a same instruction with RDTSCP creates different timing values at different instances.
New RDTSCP benchmark code generates similar timing measurements.

## Slide 69: Timing Attack in Modern Systems
Nondeterminism
(performance improvements)
Requires ROOT ACCESS
Can be done from USER space
disable
disable
eliminate
disable

## Slide 70: Timing Attack in Modern Systems
How to Benchmark Code Execution Times on Intel® IA-32 and IA-64 Instruction Set Architectures - Gabriele Paoloni (White Paper)
Removes all Nondeterminism
(with root access)

## Slide 71: Timing Attack in Modern Systems
Spy thread
while(1){;}
Virtual Core 0
Virtual Core 1
Time measurement thread
start = time_fn()
/*function*/
end = time_fn()
timing = end - start
Core
Spy thread keeps one virtual core occupied and lets other thread run solely on other virtual core
Eliminate nondeterminism due to hyper-threading from user space

## Slide 72: Timing Attack in Modern Systems
Accuracy around 60%
After Removing all Indeterminism
Accuracy 0%
Timing Attack on Modern System (Core i5)

## Slide 73: Timing Analysis for Row Hammering
Cache Miss
Crypto execution
Cache Memory
DRAM

## Slide 74: Timing Analysis for Row Hammering
Rank
Banks
Rows
Slice 0
Slice 1
Slice 2
Slice 3
DRAM access on cache miss
Copies data to indexed cache set and slice

## Slide 75: Timing Analysis for Row Hammering
Slice 0
Slice 1
Slice 2
Slice 3
Rank
Banks
Rows
Once data in cache, access to same data results in Cache Hit
Next access results in Cache Miss
Access to DRAM on cache misses imposed by spy
Concurrent accesses to DRAM banks to enforce rowbuffer collision
Spy fills the cache sets with its own data

## Slide 76: New Frontiers of Micro-Architectural Attacks
.
Bypass existing Address Space Layout Randomization schemes by exploiting a side-channel created through shared BTB
Jump over ASLR
CacheBleed
Targets OpenSSL 1.0.2f RSA modular exponentiation on Intel processors using cache bank conflict

## Slide 77: New Frontiers of Micro-Architectural Attacks
Exploiting Speculative Execution
Spectre: uses branch misprediction and out-of-order execution to access unprivileged data.
01
03
Foreshadow: uses L1TF and page fault along with meltdown to retrieve data across SGX enclaves.
02
Meltdown: uses out-of-order execution and prime-probe method to access kernel pages

## Slide 78: Conclusions
Micro-architectural attacks encompasses the intersection of architecture and computer security.
Architectures have been developed to enhance performance:
  Cache memories
  Prefetchers
  Out of order execution
However leakage due to architecture is not yet a guideline for design.
More attacks are emerging and security is getting to be a game changer: Design-for-Security along with other objectives like performance, power, energy.
  Good time to think of clean paper designs for secured computer architecture
  RISC-V is a good open source platform to experiment.

## Slide 79: Thank You for your attention!!
Ref: Viewpoint, By Leah Hoffmann Communications of the ACM, June 2018, Vol. 61 No. 6, Pages 104-ff10.1145/3204453 .

## Slide 80
Please visit us at: https://www.isical.ac.in/~space2019/index.html
Proceedings in Springer LNCS

## Slide 81: Text Book on Timing Attacks
Discusses various timing attack algorithms in detail allowing readers to reconstruct the attack.
Presents the application of timing attacks on remote systems and cloud environments.
Examines information leakage models that would help quantify leakage in a covert timing channel

## Slide 82: Text Book on Fault Attacks
Reviews exhaustively the recent key research into fault tolerant architectures in hardware security and cryptography software
Discusses the latest fault attacks on a wide variety of cryptographic implementations, such as biased fault attacks, algebraic fault attacks, and attacks on authenticated encryption based ciphers
Offers hands-on and practical demonstrations for handling complex secure cryptographic architectures, complementing the theoretical analysis

## Slide 83: MOOC Course on Hardware Security
https://www.youtube.com/watch?v=xwgecIX3E4I&list=PLbRMhDVUMngfulSvKL0cT-tn8ULtERsWk&index=1